## Slide 1
Full Coverage, Hermetic. Compact. Operate in the magnetic field. Good energy resolution. Good EM+HAD Performance. Fast.
What will be in the report O.Tsai (UCLA) 5/18/2017:
BEMC
CEMC
FEMC
2
Optimization of light collection for BEMC (EM) - finished.
Anomalous signals in SiPM Run 17 – not observed.
‘Radiation’ damages of sensors for BEMC – main concern.
Preliminary, at eta~4 we see ~10^11 n/cm2, at eta~2.5 it is about 50% less.
N.B. this is for small calorimeter prototypes (calorimeter itself will be a source of neutrons)
In general, need to boost light yield and at the same time reduce volume of silicon photo-sensors, i.e. overall efficiency of light collection has to be significantly improved, especially for hcal.

## Slide 2
What will be in report cont:
As we reported last time, optimization of hcal will continue
From Pb/Sc moving to Fe/Sc (cost/neutrons)
Light collection will be redesigned – want to collect x15 more light, seemingly possible with APDs.
But need to modify sensors for our needs. Talked/talking with HPC (next week RIKEN people will have meeting with HPC in Japan).
Preliminary, HPC wants ~ $90k NRE. Idea is to split cost between STAR, sfPHENIX and EIC, each contributing $30k for this development. We want to request $30k from EIC R&D for this year.
After run17 ends (end of June) we’ll be doing lot of test with HCAL tower in the lab using exposed/fresh sensors (we have SiPMs , APDs in the STAR IP exposed for the whole Run17).
In 2018 probably two HCAL towers will be placed at IP with modified light collection and readout.
We’ll ask ~ $10k for travel to BNL to run these test.
Our report will not be ready before June 9 or so.
11